## Slide 1
DESIGN OF MACHINE ELEMENTS
Manual Lathe Machine
Carriage Guideway & Leaad Screw Design
Sonal(B22ME062) Yogesh(B22ME073)

## Slide 2
INTRODUCTION
The carriage is a major part of the lathe machine that supports and moves the cutting tool along the bed. It enables precise longitudinal and cross-feed motion during machining operations like turning, facing, and threading.
  Holds and moves the cutting tool accurately
  Enables smooth machining along the length of the workpiece
  Supports tool post and cross-slide mechanisms

## Slide 3
  Guideways & Carriage – FG260 (High-Grade Cast Iron):
    FG260 has higher hardness and improved wear resistance
    Its excellent self-lubricating and damping properties help reduce friction and absorb vibrations during carriage movement.
  Leadscrew – ANSI 1045 (Medium Carbon Steel): ANSI 1045 steel offers high tensile strength and good machinability, ideal for handling axial loads in the screw mechanism.
  Bed – FG200 (Gray Cast Iron): Its good castability and compressive strength make it ideal for the rigid and stable base structure of the lathe.
  Tool Holder – Cast Alloy Steel: Cast alloy steel offers high toughness and wear resistance, making it suitable to withstand cutting forces and shocks.
  Tool – HSS (High-Speed Steel): HSS retains hardness at elevated temperatures, ideal for cutting operations at high speeds.
MATERIAL SELECTION

## Slide 4
FORCES
REPRESENTATION

## Slide 5
  F1 : Normal Force at one V surface of carriage
  F2 : Normal Force at other V surface of carrriage
  F3 : Normal Force at flat surface carriage
  FX : X component of cutting force at tool and workpiece interface
  FY : Y component of cutting force at tool and workpiece interface
  FZ : Z component of cutting force at tool and workpiece interface
  R : Pushing force of carriage
  μF1 : Friction force due to force F1
  μF2 : Friction force due to force F2
  μF3: Friction force due to force F3
  W : Force due to weight of the carriage
  d : diameter of the workpiece
  h : vertical distance between center of workpiece and carriage surface
  b : horizontal distance between flat and V shape surface
  Z : vertical distance between V shape and lead Screw
  u,v,w : Length of contact
NOMENCLATURE OF FORCES & DISTANCES

## Slide 6
ASSUMPTIONS
  Weight of Carriage : 200 Kg
  Cutting Forces:
    Fx : 500 N
    Fy : 800 N
    Fz : 4000 N
  b (distance between guideways) = 0.12 m
  h (distance between workpiece & guideway) : 0.13 m
  d (WorkPiece Diameter) = 0.03 m
  Friction Coeff = 0.1
  R (Pushing force) = 50 N
  L (Carriage Lenght) = 0.15 m
  contact Angle(V) = 45 deg
  All dimensions are taken with reference of Manual Lathe Machine present in IIT Jodhpur Centeral Workshop
  Fx, Fy, Fz are general assumed cutting forces

## Slide 7
CALCULATION UNDER STATIC LOADS CONSIDERING MAXIMUM NORMAL STRESS
THEORY
PART - 1

## Slide 8
DERIVATION OF EQUTIONS NORMAL STRESS

## Slide 9
DERIVATION OF EQUTIONS NORMAL STRESS

## Slide 10
DERIVATION OF EQUTIONS NORMAL STRESS

## Slide 11
DERIVATION OF EQUTIONS NORMAL STRESS

## Slide 12
DERIVATION OF EQUTIONS NORMAL STRESS

## Slide 13
DERIVATION OF EQUTIONS NORMAL STRESS

## Slide 15
  These dimensions are based on Normal Shear Stress Theory
  All Calculation are done in Matlab Software
FINAL DIMENSIONS &
FINAL FORCES VALUES
  F1 = 2606 N
  F2 = 3546 N
  F3 = 1613 N
  U = 0.029 m = 2.9 cm
  V = 0.039 m = 3.9 cm
  W = 0.017 m = 1.7 cm

## Slide 16
CALCULATION FOR NOTCH SAFETY AT ‘ V ’ JUNCTION OF CARRIAGE & GUIDEWAY MATTING SURFACE
PART - 2

## Slide 17
NOTCH SAFERY DERIVATION

## Slide 18
NOTCH SAFERY DERIVATION

## Slide 19
Sigma Nominal Practical <= Sigma Nominal Theoritical
  For safe design
CALCULATION OF HEIGHT AT NOTCH CENTER
  On Calculating on matlab
b’ = 0.04 m = 4 cm
  For to be more safe we have considered (b’ = 5 cm)

## Slide 20
CALCULATION FOR NOTCH SAFETY AT ‘ V ’ JUNCTION DUE TO SHEAR
PART - 3

## Slide 21
NOTCH SAFERY DERIVATION

## Slide 22
NOTCH SAFERY DERIVATION

## Slide 23
SHEAR SAFERY DERIVATION
  On calculation on Matlab
b’ = 0.11 m = 11 cm

## Slide 24
COMPRASION OF DIMENSIONS
  From Notch sensitivity the dimension of b’ = 0.04 m = 4 cm
  From Notch sensitivity for Shear the dimension of b’ = 0.11 m = 11 cm
  To make a safe design, consider b’ = 0.11 m = 11 cm

## Slide 25
DESIGN OF LEAD SCREW
BUCKLING & TORSION CONSIDERATION
PART - 4

## Slide 26
LEAD SCREW (TORSION)

## Slide 27
LEAD SCREW (TORSION)

## Slide 28
LEAD SCREW (BUCKLING)
Assumption: Forces acting on Y-direction is critical force

## Slide 29
DIMENSIONS OF LEAD SCREW
  diameter (considering torsion) = 7.7 mm
  All calculation is done in Matlab
  length of Lead Screw = 760 cm (Basic Lab IIT Jodhpur)
  diameter (buckling) = 1.5 cm
diameter(buckling) > diameter(torsion)
  Final diameter of lead screw : 2 cm (Considering additional safety)

## Slide 30
ANALYSIS OF SOLIDWORKS
OBSERVATIONS

## Slide 32
The amplitude of buckling is of order 10^-4 mm, which is very low. So our system is safe buckling also.

## Slide 33
D
R
A
W
I
N
G
S

## Slide 34
D
R
A
W
I
N
G
S

## Slide 35
MATLAB CODE

## Slide 36
CONTRIBUTIONS
  Research and Finding about carriage and Lathe: Sonal & Yogesh
  Equlibrium equations in static analysis and Normal force equations:
    Force : Yogesh
    Moment : Sonal Raj
  Notch Sensitivity calculation
    Horizantal Component : Sonal Raj
    Vertical Component : Yogesh
  lead Screw Design (Buckling + Torsion) : Sonal Raj & Yogesh
  SolidWorks (Model & Drawing)
    Bed, Carriage, LeadScrew : Yogesh
    ToolPost, Tool, Guideways : Sonal
  Static & Buckling Anlaysis : Sonal & Yogesh

## Slide 37
THANK YOU